## Slide 1: Enhancement for Lab 3
Group 20

## Slide 2: Booth’s Algorithm (Implementation)
Check if it is unsigned or signed multiplication. Proceed only if it is a signed multiplication
Initialise variables (A, S, P)
  A: Fill the most significant bits with the value of multiplicand and the remaining bit be filled with zero
  S: Fill the most significant bits with the value of – multiplicand and the remaining bit be filled with zero
  P: Fill the most significant X bits with zeros, append the value of the multiplier and fill the least significant bit with zero
Determine the 2 least significant bits of P
  01: Find P + A
  10: Find P + S
  00: Do nothing, use P directly in next step
  11: Do nothing, use P directly in next step

## Slide 3: Booth’s Algorithm (Implementation)
4) Arithmetically shift the value obtained in the previous step by a single place to the right. Let P be now equal to this value
5) Repeat step 3 and 4 until they have been done “y” (number of bits in the multiplier) times
6) Drop the least significant bit from P. The answer is the product of the multiplier and multiplicand

## Slide 4: Booth’s Algorithm (Evaluation)
Used to multiply signed binary integers in 2’s complement
Able to do signed multiplication in 1 width cycle however, it requires 2*Width + 1 registers
Requires additional muxes to differentiate signed and unsigned multiplication
Hence, speeding up the multiplication process by reducing the number of steps required, at the exchange of using more registers